## Slide 1: Useless Machine, Useful Application
108062103 莊鈞堯
108062304 黃子軒

## Slide 2: What Is Useless Machine?
Useless Machine is a useless thing that makes you angry.
Usually, it is a box with a switch, so we also call it “useless box.”
When you try to touch the switch, the machine tries its best to trick you.
The following pictures are some examples of useless machines.

## Slide 3: What Is Useful Application?
Classic useless machines only make people angry, so we try to make it useful.
However, we still want to keep the features of classic useless machines.
We also added some more unique gameplays.
Therefore, we designed 3 modes for this useless machine:
1. Normal Switch (NS)
2. Useless Box (UB)
3. Useful Car (UC)

## Slide 4: 1. Normal Switch (NS)
Features
  You can control the switch with a Smartphone app.
  If you do so, the machine will toggle the switch by itself.
  In addtion, if you try to toggle the switch with your bare hands, then the machine will not trick you but act like a normal switch.
  The switch is able to connect to an external device, so you can control the device with the switch .

## Slide 5: 2. Useless Box (UB)
Features
  You can decide what kind of useless box you want to play with.
  3 different boxes you may choose:
    Classic, Dodge, or Advanced.
  If no choices were made, we will give you a random sequence of all modes.
  Don’t be greedy! You will see “Err” on 7-segment display if you choose more than 1 useless box, and of course, it won’t play with you.

## Slide 6: 2.1 Classic Mode
Features
  The box pushes the switch back once you toggle the switch.
  Most useless boxes are dangerous because the flipping arms may hurt you when it tries to toggle the switch but your hands are still there.
  Don’t worry! We have IR sensors detecting whether your hands are close or not, so the box will push it back only when your hands leave.

## Slide 7: 2.2 Dodge Mode
Features
  The box runs away when you try to touch the switch.
  In most situations, the box will go to the opposite side.
  It runs for about 3 seconds and then stops.

## Slide 8: 2.3 Advanced Mode
Features
  The box competes with you for toggling the switch.
  Advanced Mode is only recommended for high-level players.
  Competition means that it is dangerous because the box won’t let you win, even if your hands are still there.
  Note that the safe method in 2.1 is still applied here, but it will work only when the box wants to push the switch back after the competition ends.

## Slide 9: 3. Useful Car (UC)
Features
  It becomes a car that can be remotely controlled by the Smartphone app.
  You can let the car go Forward, Backward, Left or Right.
  When left or right is chosen, the car stay there and change direction, so it won’t go forward or backward at the same time.
  You can still toggle the switch with the Smartphone app in this mode.
  Also, the classic mode and the safety measure of the useless box still function.

## Slide 10: 4. How To Change Mode?
  1. Mode can be changed with a pushbutton (btnC) or Smartphone app, and the current mode will show on 7-segment display (NS = 0, UB = 1, UC = 2.)
  2. Use sw0～sw2 to change the useless box you want in UB mode, and LED will show what kind of useless box you want.
  3. Have Fun!

## Slide 11: Hardware Design Goals
  1. Achieve great user experience with common and low cost components.
  2. Stick to the original spec without causing permanent changes to the car provided in class.
  3. Arrange sensors for easy hand detection.
  4. Provide easy connection to the FPGA board.
  5. Can be remotely controlled.
  6. Can safely control external devices without putting the FPGA board at risk.

## Slide 12: Signal Connections and Component Choice
SR-04
Ultrasonic Sensor
Infrared
Sensor
MG996r
High-Torque
Servo
L298n H-bridge
Motor Driver
HC-05 UART
Bluetooth Module
Optical-coupled
Relay Module

## Slide 13: Power Connection
6V
---->
6V
---->
3.3V
---->
All the voltage regulator ICs on Basys3 can withstand well beyond 6V, so it’s safe (unless we want to use the USB A peripheral port).
Difficulties:
The High-Torque Servo can draw up to 2.5A each.
Risk of running components higher than their standard voltage.
It took many iterations and compromises to get the desired result.
Power source:
4x High-current AA batteries
Power Requirements:
FPGA Board: 5v servo motor: 4.8~7.2v
IR sensors: 3~6v DC motor: 5~12v
Ultrasonic seneor: 5v Relay module: 5v
Bluetooth : 3.3v or 5v motor driver: 3.3~7v

## Slide 14: Simplified Connections and Reusable Car
  1. Hand Soldered circuit board to handle all power connections and convert all signals to PMOD pinout.
  2. FPGA Board can be removed easily removed at any time.
  3. All the cable mess is hidden under the box.
  4. The wooden box is secured to the car with four standard screws and can be removed without affecting other functions of the machine.

## Slide 15: Responsibility
108062103 莊鈞堯
  Hardware design , build and maintenance.
  Bluetooth connection and smartphone App.
  Verilog modules to communicate with external devices.
108062304 黃子軒
  State machine design and debug.
  Top Verilog module design.
  Design player detection algorithms with existing sensors.
ALL
  PowerPoint.
  System test.
  Debug.

## Slide 16: Thank You For Your Listening!